## Slide 1: Learning from accidents: an introduction to railway signalling in the UK
Dr Robin Wilson

## Slide 3
What is the purpose of signalling?
Get trains to the right place
Get them there safely

## Slide 6
Points

## Slide 8
Do we need a signaller?
Maybe not?
Not many trains ➔ Unlikely to hit each other
Get out and change the points manually when needed

## Slide 10
Liverpool and Manchester Railway
Opened 1830
First intercity passenger railway
Policemen – security + signalling
(‘Bobbies’)
Spaced every mile along track
Arm signals, then red/green flags
Simple levers for points

## Slide 14
Accident: Abbots Ripton
Date: 1876
Location: East Coast Main Line, Huntingdonshire
Deaths: 13 Injuries: 53

## Slide 15
Accident: Abbots Ripton
Date: 1876
Location: East Coast Main Line, Huntingdonshire
Deaths: 13 Injuries: 53
Signals froze at ‘proceed’
Changes since:
Different type of semaphore
Keep signals at ‘danger’ until they need to be cleared
Better brakes

## Slide 16
But how did they know whether to stop a train or not?
< 10 minutes since last train went past?
Stop train
10-17 minutes since last train?
Proceed at caution
> 17 minutes
Proceed
Time-interval working

## Slide 17
Not fail-safe – lots of accidents!

## Slide 18
Communication helps
Electric Telegraph
Send pulses down a wire, moves a needle
Can send messages using a code
First installed 1837
Used to catch a murderer in 1845

## Slide 19
1
2
3
4

## Slide 20
1
2
3
4
Train out of section

## Slide 21
1
2
3
4

## Slide 22
1
2
3
4
Block Section
Absolute Block
Offer / Accept
Train entering section / Train out of section

## Slide 23
Mechanical Signalling: Semaphore signals
Two types of signals: distant and stop/home
Different railway companies couldn’t agree on up/down!
Notes: Hundreds of companies
Big Four in 1923
BR in 1948

## Slide 24
Mechanical signalling: Signal box

## Slide 25
Mechanical signalling: Lever frame
Stop signals Distant signals Points Point locks Spare

## Slide 26
Mechanical signalling: Diagram

## Slide 27
Mechanical signalling: Diagram

## Slide 28
Mechanical Signalling: Rods and wires
1 mile for signals, 350 yards for points ➔ lots of signal boxes

## Slide 29
5 miles – 7 signal boxes

## Slide 30
Mechanical Signalling: Interlocking
Stops you setting conflicting signals/points
For example:
Must set and lock all points before signal can be cleared
Must set distant to ‘caution’ before setting stop signal to ‘stop’

## Slide 31
Mechanical Signalling: Block Bells
1 Call attention
2 Train entering section
2-1 Train out of section
3-1 Is line clear for train?
6 Obstruction danger
and many more…

## Slide 32
Mechanical Signalling: Block instruments

## Slide 33
Mechanical Signalling
This combination of ‘lock and block’ (interlocking and absolute block) mandated by Regulation of Railways Act in 1889

## Slide 34
Exeter West - Video

## Slide 35
Still in use!
373 mechanical signal boxes in 2015!

## Slide 36
Severn Bridge Junction, Shrewsbury

## Slide 37
Severn Bridge Junction, Shrewsbury
180 levers (90 in operation now)

## Slide 38
Severn Bridge Junction, Shrewsbury

## Slide 39
Moreton-in-Marsh

## Slide 40
Moreton-in-Marsh

## Slide 41
Where are the trains?
You know the train is in a specific section…
…but where exactly is it?
Is it stopped at a signal waiting for you to clear it?
Is it broken down in the middle of the section?
Is it sitting over some points?
Is it on the main line, or on the siding?

## Slide 42
LOOK!

## Slide 43
Rule 55
“If a train is brought to a stand at a signal, then after three minutes (or immediately in rain, fog or snow) the driver must dispatch his fireman or guard to the signal box to ensure the signalman was aware of the presence of the train, and that all safeguards to protect it have been put in place. The crewman must then sign the train register.”

## Slide 44
Lever collars

## Slide 45
Accident: Quintinshill
Date: 1915
Location: near Gretna Green, Scotland
Deaths: 226 Injuries: 246 Worst in the UK

## Slide 59
Accident: Quintinshill
Date: 1915
Location: near Gretna Green, Scotland
Deaths: 226 Injuries: 246 Worst in the UK
Causes:
Signalman forgot about a train – even though it was right outside his signal box!
Driver did Rule 55, but didn’t check signalman had used a lever collar
Shift change irregularities, unauthorised people in box

## Slide 60
Track Circuits – no train

## Slide 61
Track Circuits – no train

## Slide 62
Track Circuits – no train

## Slide 63
Track Circuits – no train

## Slide 64
Track Circuits – with train
Fail safe!

## Slide 65
Interlocking with points & signals
Stop points moving when a train is over them
Can’t clear signals if a train is in the way
Installed only in some places – from as early as 1870, but mostly from 1900s onwards

## Slide 66
Leaves on the line
Reduce grip – harder to stop
Insulation – interrupt the track circuit

## Slide 67
Rail Head Treatment Train

## Slide 68
Axle Counters
Count number of axles passing the counter at beginning and end of section

## Slide 69
Axle Counters
If count in = count out then the section is empty

## Slide 70
Accident: Severn Tunnel
Date: 1991
Location: Severn Tunnel
Deaths: 0 Injuries: 185

## Slide 71
Accident: Severn Tunnel
Date: 1991
Location: Severn Tunnel
Deaths: 0 Injuries: 185
Causes:
Signalling fault meant special arrangements were in place
Signalling technicians probably ‘reset’ the axle counter while there was a train in section – making the signalling system think the section was clear

## Slide 72
Colour Light Signals
Earliest installation: 1926 (Southern Region)
Other regions mostly in 50s-70s
Notes: Benefits:
More than just stop/go – multiple aspect
Can be controlled from a long way away – centralization

## Slide 73
Four Aspect Signalling: Stop

## Slide 74
Four Aspect Signalling: Caution

## Slide 75
Four Aspect Signalling: Prelim. Caution

## Slide 76
Four Aspect Signalling: Clear

## Slide 78
Electrical lever frames
As early as 1900
Mostly 1920s-1950s
Liverpool Lime Street frame still in use until 2018!

## Slide 79
NX Panels
1960s
Replaced 40 signal boxes!
80 miles of track
Fully track-circuited

## Slide 80
NX Panels

## Slide 81
NX Panels

## Slide 82
Oxford Panel (closed in 2018)
Notes: Southbourne is under Chichester Panel
Emsworth is under Havant ASC

## Slide 83
Gloucester Panel

## Slide 84
NX Panels

## Slide 85
NX Panels

## Slide 86
NX Panels

## Slide 87
Relay interlocking

## Slide 88
Accident: Clapham Junction
Date: 1988
Location: South of Clapham Junction station
Deaths: 35 Injuries: 484

## Slide 89
Train 1
Train 2
Train 3
Accident: Clapham Junction
Train 2
Train 1
Train 3
To Southampton
To London

## Slide 90
Accident: Clapham Junction
Date: 1988
Location: South of Clapham Junction station
Deaths: 35 Injuries: 484
Causes:
Signalling upgrades taking place in the area
‘False feed’ in relay room from stray wire – ‘wrong side’
Meant the relay was powered regardless of track circuit state
Signalling technician had been working 7 days a week for 13 weeks!
No proper checking and wire counting

## Slide 91
Accident: Clapham Junction
Date: 1988
Location: South of Clapham Junction station
Deaths: 35 Injuries: 484
Changes since:
Working hours limits
Mandatory testing
Gradual move to solid-state interlocking
Radio communications with trains – emergency stop
But… Waterloo accident in 2017: have lessons been learnt?

## Slide 93
Driver Error
Signal Passed At Danger
(SPAD)

## Slide 94
Accident: Harrow and Wealdstone
Date: 1952
Location: Harrow and Wealdstone station, London
Deaths: 112 Injuries: 340

## Slide 95
Train 1
Train 2
Train 3
Accident: Harrow and Wealdstone
Station
Train 2
Train 1
Train 3

## Slide 96
Accident: Harrow and Wealdstone
Date: 1952
Location: Harrow and Wealdstone station, London
Deaths: 112 Injuries: 340
Causes:
Driver passed a colour-light signal at caution
Then two semaphores at danger
Don’t know why: driver and fireman died

## Slide 97
Train Stops

## Slide 98
Train Stops

## Slide 99
Automatic Warning System (AWS)
Gradually installed 1950s-1980s – at nearly all signals now

## Slide 100
Accident: Ladbroke Grove
Date: 1999
Location: near Paddington station, London
Deaths: 31 Injuries: 523

## Slide 101
Train 1
Train 2
To Paddington
To Slough

## Slide 102
Train 1
Train 2
To Paddington
To Slough

## Slide 103
Train 1
Train 2
To Paddington
To Slough

## Slide 104
Train 1
Train 2
To Paddington
To Slough

## Slide 105
Train 1
Train 2
To Paddington
To Slough

## Slide 106
Train 1
Train 2
To Paddington
To Slough

## Slide 107
Train 1
Train 2
To Paddington
To Slough

## Slide 108
Accident: Ladbroke Grove
Date: 1999
Location: near Paddington station, London
Deaths: 31 Injuries: 523
Causes:
SPAD
AWS doesn’t always help
Frequently SPAD-ed signal (8 times in 6 years)
Poor signal sighting
Inexperienced driver – poor training
No flank protection
Poor signaller response

## Slide 109
Train Protection & Warning System (TPWS)
Overspeed & SPAD (and for buffer stops)
Finished installation at high-risk locs by 2004
80% reduction of high-severity SPADs

## Slide 110
‘Modern’ signalling – IECCs & ROCs

## Slide 111
‘Modern’ signalling – IECCs & ROCs
Automatic Route Setting

## Slide 112
Thames Valley Signalling Centre

## Slide 113
In-Cab Signalling
Cambrian Coast line – ETCS Level 2

## Slide 114
In-Cab Signalling

## Slide 115
In-Cab Signalling

## Slide 116
Fixed Block
Train 1
Train 2
Train 1
Train 2
High speed
Moving Block

## Slide 117
Fixed Block
Train 1
Train 2
Train 1
Train 2
Low speed
Moving Block

## Slide 118
Automatic Train Operation (ATO)
Victoria Line – first major ATO installation (1968)
(Fixed Block)

## Slide 119
Automatic Train Operation (ATO)
Victoria Line – first major ATO installation (1968)
(Fixed Block)

## Slide 120
Automatic Train Operation (ATO)
Docklands Light Railway – No Driver!
(Moving Block since 1994)

## Slide 121
‘Modern’ signalling – a mixture!

## Slide 122
Thank you
robin@rtwilson.com
Find out more at:
Swindon Panel @ Didcot Railway Centre
Preserved Railways
Signals to Danger podcast
Come and play with some demos!